## Slide 1: Chapter 3: The Data Link Layer

## Slide 2: Terminology: Packets and Frames
Header | Payload field | Trailer
Frame
Sending machine
Packet
Packet
Receiving machine
Header | Payload field | Trailer
Network
Data Link
Fig: Relationship between packets and frames
Each frame contains a frame header, a payload field for holding the packet, and a frame trailer.
Header | Packet | Trailer
Frame

## Slide 3: Layered Communication
4
3
2
1
4
3
2
1
4
3
2
1
4
3
2
1
Host 1
Host 2
Host 1
Host 2
Virtual Data Path
Actual data path
Fig :(a) Virtual communication. (b) Actual communication.

## Slide 4: Data Link Layer
Reliable bitstream between adjacent computers
  Design Issues
  Error Detection and Correction
  Elementary Protocols
  Sliding Window Protocols Protocol Verification
  Example Data Link Protocols

## Slide 5: Design Issues
Providing a well-defined service interface to the network layer.
Dealing with transmission errors.
Regulates flow of data so slow receivers are not swamped by fast senders.

## Slide 6: Kinds of Services
Unacknowledged connectionless service
no error detection or recovery appropriate when error rate is very low
real-time – late data are worse than bad data
Acknowledged connectionless service
each packet is acknowledged
retransmit after timeout expires optimization when errors are frequent
Acknowledged connection-oriented service
number frames to detect duplicates
connection setup, transmission, connection release

## Slide 7: Framing
Breaking up the bit stream into smaller, manageable units known as frames is called framing.
Four methods of framing are:
  1. Byte count.
  2. Flag bytes with byte stuffing.
  3. Flag bits with bit stuffing.
  4. Physical layer coding violations.

## Slide 8: Framing (Byte Count)
(b)
5 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 8 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 8 | 7 | 8 | 9 | 0 | 1 | 2 | 3
5 | 1 | 2 | 3 | 4 | 7 | 6 | 7 | 8 | 9 | 8 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 8 | 7 | 8 | 9 | 0 | 1 | 2 | 3
How to mark the start and end of each frame?
Character count: field in header for frame size
Character count One character
(a)
Error
Frame 1
5 characters
Frame 1
Frame 2
5 characters
Frame 2 (Wrong)
Frame 3
8 characters
Frame 4
8 characters
Now a character count
Transmission errors are problematic

## Slide 9: Framing (Byte Count)
(b)
5 | 1 | 2 | 3 | 4 | 7 | 6 | 7 | 8 | 9 | 8 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 8 | 7 | 8 | 9 | 0 | 1 | 2 | 3
Error
Frame 1
Frame 2 (Wrong)
Now a character count
Problem of Byte Stuffing:
Count Vulnerability: The byte count can be garbled by a transmission error.
Error Detection Doesn't Solve It: Even if a checksum indicates that the frame is bad, the destination cannot determine the start of the next frame.
Retransmission Challenge: Sending a frame back to the source for retransmission is ineffective because the destination does not know how many bytes to skip to reach the start of the retransmitted frame.
Due to these challenges, the byte count method is rarely used as the sole framing technique in data communication.

## Slide 10: Framing (Flag bytes with byte stuffing)
In byte stuffing, a special reserved control character (often called the "flag" byte) is chosen to denote the beginning and end of a frame.
Two consecutive flags indicate the end and start of the frame. Thus, if the receiver ever loses synchronization it can just search for two flag bytes to find the end of the current frame and the start of the next frame.
FLAG | Header | Payload field | Trailer | FLAG
FLAG | Header | Payload field | Trailer | FLAG
Flag Byte: 01111110

## Slide 11: Framing (Flag bytes with byte stuffing)
Problem: It may happen that the flag byte occurs in the data. We need to prevent this flag byte (within the data) from being misinterpreted as the starting or ending of a frame.
Solution: Byte stuffing.
Byte stuffing is a technique where a special escape sequence is used to represent the flag byte when it appears in the data.
This ensures that the flag byte within the data is not misinterpreted as a frame delimiter.
A
B
ESC
FLAG
A
B
ESC
ESC
A
ESC
B
ESC
ESC
FLAG
A
ESC
B
ESC
ESC
ESC
B
A
FLAG
B
A
ESC
FLAG
A
ESC
B
ESC
A
ESC
B
Escape conventions (stuffing)
Original characters
After stuffing

## Slide 12: Framing (Byte Stuffing)
Problem 3. The following data fragment occurs in the middle of a data stream for which the bytestuffing algorithm described in the text is used:
A B ESC C ESC FLAG FLAG D.
What is the output after stuffing?
Solution: After stuffing, we get
A B ESC ESC C ESC ESC ESC FLAG ESC FLAG D.
Disadvantages of Byte Stuffing:
  tied to the use of 8-bit bytes.
  length of a frame now depends on the contents of the data it carries.

## Slide 13: Framing (Bit Stuffing)
Flags with bit stuffing
Flag is 01111110
(a) 0 1 1 0 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 0 0 1 0
(b) 0 1 1 0 1 1 1 1 1 0 1 1 1 1 1 0 1 1 1 1 1 0 1 0 0 1 0
Stuffed bits
(c) 0 1 1 0 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 0 0 1 0
Byte/Bit stuffing is done only in the data portion, not in the starting and ending flags.
With bit stuffing, the boundary between two frames can be unambiguously recognized by the flag pattern.
Side effect of both Byte Stuffing and Bit Stuffing: the length of a frame now depends on the contents of the data it carries.

## Slide 14: 3.1.3 Error Control
Receiver provides feedback in the form of positive or negative acknowledgements (ACKs)
Dropped frames are handled using timeouts
Dropped transmissions or ACKs are handled by retransmitting
Duplicate frames are handled using sequence numbers.

## Slide 15: 3.1.4 Flow Control
->Slowing down a fast sender
Two approaches are commonly used
  feedback-based flow control:
    The receiver sends back information (feedback) to the sender giving it permission to send more data, or at least telling the sender how the receiver is doing.
  rate-based flow control
    Here, the protocol has a built-in mechanism that limits the rate at which senders may transmit data, without using feedback from the receiver.
.

## Slide 16: Data Link Layer
Reliable bitstream between adjacent computers
  Design Issues
  Error Detection and Correction
  Elementary Protocols
  Sliding Window Protocols Protocol Verification
  Example Data Link Protocols

## Slide 17: 3.2 Error Detection and Correction
Network designers have developed two basic strategies for dealing with errors. Both add redundant information to the data that is sent.
One strategy is to deduce what the transmitted data must have been: Error Correction
The other is to only deduce that an error has occurred (but not which error); Error Detection
Neither error-correcting codes nor error-detecting codes can handle all possible errors.
Error correcting is used on unreliable links
Error detecting (enough to know something went wrong) is used on reliable links. Just retransmission.

## Slide 18: 3.2 Error Detection and Correction
Types of Errors: Errors can be of three types, namely single bit errors, multiple bit errors, and burst errors.
Single bit error − In the received frame, only one bit has been corrupted, i.e. either changed from 0 to 1 or from 1 to 0.
Multiple bits error − In the received frame, more than one bits are corrupted.
Burst error − In the received frame, more than one consecutive bits are corrupted. (Common)

## Slide 19: 3.2 Error Detection and Correction
We will examine three different error-detecting codes. They are all linear, systematic block codes:
  1. Parity.
  2. Checksums.
  3. Cyclic Redundancy Checks (CRCs).
Parity Check
The parity check is done by adding an extra bit, called parity bit to the data to make a number of 1s either even in case of even parity or odd in case of odd parity.
In case of even parity: If the number of 1s is even then parity bit value is 0. If the number of 1s is odd then parity bit value is 1.
In case of odd parity: If the number of 1s is odd then parity bit value is 0. If the number of 1s is even then parity bit value is 1.
The parity check is suitable for single bit error detection only.
Notes: On receiving a frame, the receiver counts the number of 1s in it. In case of even parity check, if the count of 1s is even, the frame is accepted, otherwise, it is rejected. A similar rule is adopted for odd parity check.

## Slide 20: 3.2 Error Detection and Correction
Even parity

## Slide 21
The data is divided into k segments each of m bits.
In the sender’s end the segments are added using 1’s complement arithmetic to get the sum. The sum is complemented to get the checksum.
The checksum segment is sent along with the data segments.
At the receiver’s end, all received segments are added using 1’s complement arithmetic to get the sum. The sum is complemented.
If the result is zero, the received data is accepted; otherwise discarded.
Checksum

## Slide 22: Cyclic redundancy check (CRC)
Unlike checksum scheme, which is based on addition, CRC is based on binary division.
In CRC, a sequence of redundant bits, called cyclic redundancy check bits, are appended to the end of data unit so that the resulting data unit becomes exactly divisible by a second, predetermined binary number.
At the destination, the incoming data unit is divided by the same number. If at this step there is no remainder, the data unit is assumed to be correct and is therefore accepted.
A remainder indicates that the data unit has been damaged in transit and therefore must be rejected.

## Slide 24: Hamming Codes, 1950
Codeword, n bits = m message (data) bits + r redundant (check) bits
A code is a set of codewords; consider a code with only four valid codewords:
  0000000000, 0000011111, 1111100000, and 1111111111
Hamming distance
  count of corresponding bits that differ
  e.g., 10001001 and 10110001 have a distance 3
  10001001
  Xor 10110001
  00111000
  if the distance is d, d single bit errors are needed to convert one to the other
3.2 Error Detection and Correction

## Slide 25: Hamming Codes Definitions
The Hamming distance for a set of code words is the minimum Hamming distance for any two codewords in the code. For these 4 codewords, what is the hamming distance?
0000000000, 0000011111, 1111100000, and 1111111111
To reliably detect d single bit errors, the code must have distance d+1
To correct d single bit errors, the code must have distance 2d+1, to ensure that the original codeword is closer than any other

## Slide 26: Hamming Codes
To reliably detect d single bit errors, the code must have distance d+1
0000000000, 0000011111, 1111101010, and 1111111111
Here, minimum Hamming distance: 3 ( value of d=2)
So a maximum 2 single-bit errors can be detected reliably.
Hamming distance between Codewords 1 and 2: 5 (five bits differ).
Hamming distance between Codewords 1 and 3: 7 (seven bits differ).
Hamming distance between Codewords 1 and 4: 10 (ten bits differ).
Hamming distance between Codewords 2 and 3: 8 (eight bits differ).
Hamming distance between Codewords 2 and 4: 5 ( five bits differ).
Hamming distance between Codewords 3 and 4: 3 (3 bits differ).

## Slide 27: Hamming Codes
To reliably detect d single bit errors, the code must have distance d+1
0000000000, 0000011111, 1111101010, and 1111111111
Here, minimum Hamming distance: 3 ( value of d=2)
So a maximum 2 single-bit errors can be detected reliably.
Case 1 (Error-bit < 3) : Suppose, the arrived codeword is 0000000011, instead of 0000000000.
  So here 2 single-bit errors have occurred. As it doesn’t match with any valid codeword, the receiver discards it.
Case 2 (Error-bit= 3) : Suppose, the arrived codeword is 0101011111, instead of 1111111111.
  So here 3 single-bit errors have occurred. As it doesn’t match with any valid codeword, the error is detected and the receiver discards it. According to the statement, you may think it shouldn’t be detected. But focus on reliably.
  If the arrived codeword is 1111101010, here also 3 single-bit errors have occurred. However, this time error can not be detected. When the number of error bits and hamming distance matches, both cases can happen. So detection becomes unreliable.
Case 3 (Error-bit> 3) : Suppose, the arrived codeword is 1000100111, instead of 1111111111.
  So here 5 single-bit errors have occurred, the error is detected and the receiver discards it. But, if the arrived codeword is 0000011111, here also 5 single-bit errors have occurred. However, this time error can not be detected. So sometimes it can be, sometimes not (unreliable).

## Slide 28: Hamming Codes
To correct d single bit errors, the code must have distance 2d+1, to ensure that the original codeword is closer than any other
0000000000, 0000011111, 1111100010, and 1111111111
Here, minimum Hamming distance: 5 ( value of d=2)
So double-bit errors can be corrected.
if the arrived codeword is 0000000111, after correcting two bits we can say that the original must have been 0000011111
Hamming distance between Codewords 1 and 2: 5 (five bits differ).
Hamming distance between Codewords 1 and 3: 5 (five bits differ).
Hamming distance between Codewords 1 and 4: 10 (ten bits differ).
Hamming distance between Codewords 2 and 3: 10 (ten bits differ).
Hamming distance between Codewords 2 and 4: 5 (five bits differ).
Hamming distance between Codewords 3 and 4: 5 (five bits differ).

## Slide 29: Hamming Codes
Attaining a code with minimal n
Bits 1, 2, 4, 8, 16, . . . are used as parity bits
Bits 3, 5, 6, 7, 9, 10, 11, . . . are used for the message
For k  ci2i, bit is position k is checked by bit in positions 2i where ci 0

## Slide 30: Hamming Codes (5 of 8)
1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11
 |  | 1 |  | 0 | 0 | 0 |  | 0 | 0 | 1
R1/P1: P1 10001( p1 will be 0 to make it even)
R2/P2: P2 10001(p2 will be 0 to make it even parity)
R3/P4: P4 000( p4 =0)
R4/P8: P8 001( p8=1)

## Slide 31: Hamming Codes
p1 | p2 | m3 | p4 | m5 | m6 | m7 | p8 | m9 | m10 | m11
0 | 0 | 1 | 0 | 1 | 0 | 0 | 1 | 0 | 0 | 1
Similar Even parity calculation to find the position:
R1: 011001( R1 should be1 to make it even)
R2: 10001(R2 should be 0 to make it even )
R3: 0100( R3 should be 1)
R4: 1001( R4 should be 0)
Error found in 0101 position
**R1,R2,R3 represent the redundant bits, it can also be known as parity bit

## Slide 32
P1 | p2 | m3 | p4 | m5 | m6 | m7 | p8 | m9 | m10 | m11 | m12
1 | 0 | 1 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 1 | 0
Similar Even parity calculation to find if any error has been occurred or not:
P1: 110001( will be 1 to make it even, Error detected)
P2: 011011( will be 0 to make it even parity, No error)
P4: ( =0, No error)
P8: 1011( =1, Error detected)
If the Calculated Parity or check bit is ‘1’, error is detected.
Now lets find out, where the error is. Error found at
Sender and Receiver have agreed upon Hamming code for error correction. Now at a certain time receiver has received the following message.
101101010110
Find out the position in which the error occurred if any error is detected.
P1/R1 1,3,5,7,9,11
P2/R2 2,3,6,7,10,11
P4/R3 4,5,6,7,12
P8/R4 8,9,10,11,12

## Slide 33: 3.3 Elementary Protocols
Three simplex protocol:
A Utopian Simplex Protocol
Simplex Stop-and-Wait Protocol for an Error-Free Channel
A Simplex Stop-and-Wait Protocol for a Noisy Channel

## Slide 34: 3.3 Elementary Protocols
3.3.1 A Utopian Simplex Protocol
It is unrealistic because it does not handle either flow control or error correction.
Its processing is close to that of an unacknowledged connectionless service.
The sender is in an infinite while loop just pumping data out onto the line as fast as it can.
The receiver is equally simple. Initially, it waits for something to happen, the only possibility being the arrival of an undamaged frame.

## Slide 35: 3.3.2 Simplex Stop-and-Wait Protocol for an Error-Free Channel
Utopian Protocol doesn’t have any flow control. To prevent the sender from flooding the receiver with frames faster than the latter is able to process, a general solution involves enabling the receiver to provide feedback to the sender.

## Slide 36: 3.3.3 A Simplex Stop-and-Wait Protocol for a Noisy Channel

## Slide 37: **3.4 Sliding Window Protocols
Piggybacking
3.4.1 One-Bit Sliding
3.4.2 Go Back N
3.4.3 Selective Repeat
The sliding window protocol is a specific approach to flow control that allows a sender to transmit a "window" of data before requiring an acknowledgment from the receiver.
Same link for data in both directions.

## Slide 38: Piggybacking

## Slide 39: Piggybacking
Wasted bandwidth on ACK channel
Interleave ACKs in reverse data channel (it’s probably there)
Piggybacking–add ACKs in the header of outgoing data packets
Issue: how long to wait for an outgoing data packet

## Slide 40: Bidirectional protocol: Sliding Window of Size 1
Sender
Receiver
 |  | 7 | 0 |  |  |  |  | 7 | 0 |  |  |  |  | 7 | 0 |  |  |  |  | 7 | 0 |  | 
6 |  |  |  |  | 1 | 6 |  |  |  |  | 1 | 6 |  |  |  |  | 1 | 6 |  |  |  |  | 1
5 |  |  |  |  | 2 | 5 |  |  |  |  | 2 | 5 |  |  |  |  | 2 | 5 |  |  |  |  | 2
 |  | 4 | 3 |  |  |  |  | 4 | 3 |  |  |  |  | 4 | 3 |  |  |  |  | 4 | 3 |  | 
7
6
1
5
2
0
4
3
7
6
1
5
2
0
4
3
7
6
1
5
2
0
4
3
7
6
1
5
2
0
4
3
(a) (b) (c) (d)
(a) initial; (b) after first frame sent; (c) first frame received; (d) first frame acknowledged

## Slide 41: Sliding Window Protocol
The essence of all sliding window protocols is that at any instant of time, the sender maintains a set of sequence numbers corresponding to frames it is permitted to send. These frames are said to fall within the sending window. Similarly, the receiver also maintains a receiving window corresponding to the set of frames it is permitted to accept.
The sender’s window and the receiver’s window need not have the same lower and upper limits or even have the same size.
The sequence numbers within the sender’s window represent frames that have been sent or can be sent but are as yet not acknowledged.
Already Sent and Acknowledged

## Slide 42: 3.4.1 One-Bit Sliding Window Protocol
Window Size, W=1 (Both Sender & Receiver)
Similar to stop-and-wait
Two circumstances can happen:
  Under normal circumstances, one of the two data link layers goes first and transmits the first frame. No combination of lost frames or premature timeouts can cause the protocol to deliver duplicate packets to either network layer, to skip a packet, or to deadlock. The protocol is correct. (No duplicate)
  In a peculiar situation, both sides simultaneously send an initial packet which causes synchronization difficulty. (Many duplicates)

## Slide 43: One-Bit Sliding Window Normal Case
Notation: (frame sequence, ack, packet)
A sends (0, X, A0)
B gets (0, X, A0)*
B sends (0, 0, B0)
A gets (0, 0, B0)*
A sends (1, 0, A1)
B gets (1, 0, A1)*
B sends (1, 1, B1)
A gets (1, 1, B1)*
A sends (0, 1, A2)
B gets (0, 1, A2)*
B sends (0, 0, B2)
A gets (0, 0, B2)*
A sends (1, 0, A3)
B gets (1, 0, A3)*
B sends (1, 1, B3)
Time
An asterisk indicates where a network layer accepts a packet.
The acknowledgement field contains the number of the last frame received without error.
Here we don’t know what frame, A has received without error previously. So assume the acknowledgement field is X, we can also assume it as 1.
Acknowledgment for frame 0
Now we know last frame that was received without error is 0.
Acknowledgment for frame 1

## Slide 44: One-Bit Sliding Window Degenerate Case
B sends (0, 1, B0)
B gets (0, 1, A0) *
B sends (0, 0, B0)
B gets (0, 0, A0)
B sends (1, 0, B1)
B gets (1, 0, A1)*
B sends (1, 1, B1)
B gets (1, 1, A1)
B sends (0, 1, B2)
A sends (0, 1, A0)
A gets (0, 1, B0)*
A sends (0, 0, A0)
A gets (0, 0, B0)
A sends (1, 0, A1)
A gets (1, 0, B1)*
A sends (1, 1, A1)
Half of the frames contain duplicates, even though there are no transmission errors.

## Slide 45: Pipelining
Want to avoid stalls in transmission
in one-bit sliding window, we wait a full round trip between
packet sends
Make sender window large when:
bandwidth is high or
the round-trip time is high bandwidth x round-trip time
line utilization =
l /(l bR)
l is the frame size (in bits)
b is the channel capacity (in bits/sec)
R is the round-trip time (in sec)
If l<bR the efficiency is less than 50%
The technique of keeping multiple frames in flight is an example of pipelining.

## Slide 46: Receiver Window Size is One
0
1
0
1
2
3
4
5
6
7
8
2
3
4
5
6
7
8
2
3
4
5
6
7
8
9
Timeout interval
Error
E D D D D D D
Frames discarded by data link layer
Ack 0
Ack 1
Time
Ack 2
Ack 3
Ack 4
Ack 5
Ack 6
Ack 7
Leads to Go-back n
In Go-Back-N ARQ, the size of the sender is N and the size of the receiver window is always 1.
Pipelining frames over an unreliable communication channel raises some serious issues.
First, what happens if a frame in the middle of a long stream is damaged or lost?
  Large numbers of succeeding frames will arrive at the receiver before the sender even finds out that anything is wrong.
Dealing with Error

## Slide 47: Go-Back-N Practice Q
Station A needs to send a message consisting of 9 packets to station B using a sliding window (window size 3) and go back n error control strategy. All packets are ready and immediately available for transmission. If every 5th packet that A transmits gets lost (but no ACKs from B ever get lost), then what is the number of packets that A will transmit for sending the message to B?
Ans=16

## Slide 48: Receiver’s Window is Large
0
1
0
1
9
10
11
12
13
14
E
2
3
4
5
2
6
7
8
9
10
11
12
13
14
15
8
Error
Frames buffered by data link layer
Ack 0
Ack 1
4
5
2
3
6
Nak 2
Ack 1
Ack 1
Ack 5
7
Ack 6
Ack 7
Ack 8
Ack 9
Ack 12
Ack 13
Ack 10
Ack 11
Leads to selective repeat (So in Selective Repeat Receiver window is larger than one)
tradeoff bandwidth and buffer capacity
Dealing with Error

## Slide 49: Problem for Selective Repeat
Sender
Receiver
0 1 2 3 4 5 6
7
0 1 2 3 4 5 6
7
0 1 2 3 4 5 6
7
0 1 2 3 4 5
6
7
(a) (b)
(a) initial situation window size is 7; (b) 7 frames sent, received, but not acknowledged (acknowledgment lost);
Here, the sender is permitted to transmit up to seven frames before being required to wait for an acknowledgment
If acknowledgments are lost, the sender eventually times out and retransmits Frame.
After the receiver advanced its window, the new range of valid sequence numbers overlapped with the old one, so retransmitted frames will fall in the new window. Consequently, the following batch of frames might be either duplicates (if all the acknowledgments were lost) or new ones (if all the acknowledgments were received). The poor receiver has no way of distinguishing these two cases.
Overlapped

## Slide 50: Solution
Make sure that after the receiver has advanced its window, there is no overlap with the original window.
To ensure that there is no overlap, the maximum window size should be at most half the range of the sequence numbers.
Sender
Receiver
0 1 2 3
4 5 6 7
0 1 2 3
4 5 6 7
0 1 2 3
4 5 6 7 0 1 2 3
4 5 6 7
(c) (d)
(c) initial situation, widow size is 4; (d) all frames sent,
received, but not acknowledged
No Overlap

## Slide 51: Difference between the Go-Back-N ARQ and Selective Repeat ARQ
Go-Back-N ARQ | Selective Repeat ARQ
The size of the sender is N and the size of the receiver window is always 1. | The size of the sender is N and the size of the receiver window is also N.
If a frame is corrupted or lost in it, all subsequent frames have to be sent again. | In this, only the frame is sent again, which is corrupted or lost.
If it has a high error rate,it wastes a lot of bandwidth. | There is a loss of low bandwidth.
It is less complex. | It is more complex because it has to do sorting and searching as well. And it also requires more storage.
It does not require sorting. | In this, sorting is done to get the frames in the correct order.
It is used more. | It is used less because it is more complex.

## Slide 52: Difference between Stop and Wait protocol and Sliding Window protocol:
S.NO | Stop-and-Wait Protocol | Sliding Window Protocol
1. | In Stop-and-Wait Protocol, sender sends one frame and wait for acknowledgment from receiver side. | In sliding window protocol, sender sends more than one frame to the receiver side and re-transmits the frame(s) which is/are damaged or suspected.
2. | Efficiency of Stop-and-Wait Protocol is worse. | Efficiency of sliding window protocol is better.
3. | Sender window size of Stop-and-Wait Protocol is 1. | Sender window size of sliding window protocol is N.
4. | Receiver window size of Stop-and-Wait Protocol is 1. | Receiver window size of sliding window protocol may be 1 or N.
5. | Stop-and-Wait Protocol is half duplex. | Sliding window protocol is full duplex.
6. | Stop-and-Wait Protocol is mostly used in low speed and error free network. | Sliding window protocol is mostly used in high speed and error-prone network.
7. | In Stop-and-Wait Protocol, the sender cannot send any new frames until it receives an acknowledgment for the previous frame. | In sliding window protocol, the sender can continue to send new frames even if some of the earlier frames have not yet been acknowledged.
8. | Stop-and-Wait Protocol has a lower throughput as it has a lot of idle time while waiting for the acknowledgment. | Sliding window protocol has a higher throughput as it allows for continuous transmission of frames.